## Slide 1: Hand-Held Environment Monitor
Hackathon IoT Project
Pan Hu
Tester
Tieto
pan.hu@tieto.com

## Slide 2: Background
With health we are interested in both indoor and outdoor air quality beside us. Though so many official monitoring station exist, they can’t offer more accurate value for our office place.
Take this opportunity we use powerful arduino open-source resources to provide a cheapest solution of nongovernmental environment monitoring.

## Slide 3: Overview
Hand-Held Environment Monitor(HHEM) is comprised of three parts:
Sampling Part
multiple sensors to supply accurate value
Analyzing Part
calculate sampling value to output value
Displaying Part
multiple ways to display monitor value

## Slide 4: Sampling
HHEM

## Slide 5: Sensors
Air Quality Sensor
Temperature and Humidity Sensor
Dust Sensor
Gas Sensor(MQ2)
HCHO Sensor

## Slide 6: Analyzing
HHEM

## Slide 7: Main Control Board

## Slide 8: Displaying
HHEM

## Slide 9: OLED & Network
OLED Display 128X64
Yun Shield Arduino

## Slide 10: Yun Shield

## Slide 11: Yun Shield Management

## Slide 12: Yun Shield in Data Transfer
Cloud Server
Yun Shield
Mobile
Sensors
Board
PC

## Slide 13: Monitor Indicator
HHEM

## Slide 14: Temperature and Humidity

## Slide 15: Dust
This Dust Sensor measures the Particulate Matter level in air by counting the Lo Pulse Occupancy time(LPO time) in given time unit. LPO time is in proportion to PM concentration. This sensor can provide you pretty reliable data for air purifier system because it's still responsive to particulates whose diameter is 1um.

## Slide 16: HCHO
HCHO Sensor is a semiconductor VOC gas sensor, which covert the circuit conductivity to the output signal that corresponding to the gas concentration. It has a very high sensitivity and stability, can be used to detect harmful HCHO in the home environment. Therefore, it’s a good assistant for you to improve indoor environment quality of life.

## Slide 17: CH4
The Grove - Gas Sensor(MQ2) module is useful for gas leakage detection (in home and industry). It is suitable for detecting H2, LPG, CH4, CO, Alcohol, Smoke or Propane. Due to its high sensitivity and fast response time, measurements can be taken as soon as possible. The sensitivity of the sensor can be adjusted by using the potentiometer.

## Slide 18: Buzzer
Buzzer, or Piezo speaker, is being used as an alarm or indicator.

## Slide 19: Air Quality

## Slide 20: Scenario

## Slide 21: Enhancement
HHEM

## Slide 22: Proposal
Human Detecting

## Slide 24
Pan Hu
Tester
Tieto
pan.hu@tieto.com